## Slide 1: Information Science
Lecture 1: Computer and Architecture, and Basic Operations in Computer Science
Asst. Prof. Chawanat Nakasan | 2021-10-05
GSCI1801A

## Slide 2: Agenda
What’s a computer?
What’s inside a computer?
  Explanation of various components
Computer Architecture
Binary Number System
Arithmetic Operations
Logical Operations

## Slide 3: What’s a computer?
a machine that can be programmed to manipulate symbols. Its principal characteristics are:
  It responds to a specific set of instructions in a well-defined manner.
  It can execute a prerecorded list of instructions (a program).
  It can quickly store and retrieve large amounts of data.
https://www.cs.cmu.edu/~fgandon/lecture/uk1999/computers_types/

## Slide 4: How fast is a computer?
ENIAC, 1945 (USA)
Speed: 5,000 cycles per second
ABCI, 2018 (Japan)
Speed: 37 PFLOPS (high precision real numbers)
In less than a century, world-leading computers got faster by at least 7 billion-fold.

## Slide 5: What’s in a (typical) computer?
Expansion (PCI)
GPU(s)
SSDs (card type)
Extra I/O
Extra Network
Primary Memory
(RAM)
Heatsink & Fan
Power Supply
I/O
USB Ports
Network Interface
Sound Jack
etc.
Secondary Memory: SATA Ports
HDDs & SSDs (cable type)
Other devices (BD, DVD, …)
CPU
Motherboard
Notes: Secret Question:
Can you have multiple GPUs? How do they work?
Can you have multiple network interfaces? How do they work?

## Slide 6: Basic Computer Architecture [[von Neumann Architecture]]
Processor (“CPU”)
Input Devices
Output Devices
Storage
(May be on or off motherboard)
Control Unit (CU)
Arithmetic Logic Unit (ALU)
Registers and Cache (considered as storage on CPU)
Examples of Storage: RAM Hard Drives Removable Storage
Examples of Output: Display Sound Printer Network Interface*
Examples of Input: Keyboard Mouse Network Interface*
*Network Interface is a funny oddball and will be greatly explained later!

## Slide 7: Memory Hierarchy
In CPU
On Board
Register
Cache
RAM
Solid-State Drives (SSD) (card type)
In Enclosure
Hard-Disk Drive
Solid-State Drives (SSD) (cable type)
External / Removable
faster, smaller, more expensive
slower, larger more affordable
Removable Media Back-Up Drives Networked Storage

## Slide 8: Binary number system

## Slide 9: Binary Number System
Conversion from/to Decimal
Representing negative numbers
Why it’s easier than decimal?
Binary systems in the nature

## Slide 10: What is decimal number?
4,482,692,653
4,000,000,000
400,000,000
80,000,000
2,000,000
600,000
90,000
2,000
600
50
3
4×109
4×108
8×107
2×106
6×105
9×104
2×103
6×102
5×101
3×100

## Slide 11: Now, what is binary number?
11101010
10000000
1000000
100000
00000
1000
000
10
0
1×27 = 128
1×26 = 64
1×25 = 32
0×24 = 0
1×23 = 8
0×22 = 0
1×21 = 2
0×20 = 0
>> This part is decimal
234

## Slide 12: Indicating Numbers by Bases
100011012
10001101
1000110110
0b10001101
Programming Style
Using Subscripts
Binary Numbers (“bin”)
Decimal Numbers (“dec”)

## Slide 13: A Bit and a Byte
100011012
This is a bit.
8 bits make a byte.
Bit is the smallest digital information possible.
A lot more meaningful data in computers are in bytes, such as characters (1 or 2 bytes) and numbers (1-8 bytes).
Files are almost never stored by individual bits.
Notes: Note that a byte used to consist of more or less than 8 bits. Nowadays, it is commonly accepted that 8 bits make a byte, and a character (ASCII. We might get to learn about Unicode later.) is encoded on a per-byte basis.

## Slide 14: Conversion Methods
Binary to Decimal
Decimal to Binary
Position value method (earlier)
Short division method
Position value method
Notes: The position value method is just math we showed earlier. The fun method is the short division.

## Slide 15: Decimal to Binary by Short Division
223 = ?2
223
112 1
2
Remainder

## Slide 16: Decimal to Binary by Short Division
223 = ?2
223
112 1
56 0
2
2
Please continue dividing until you reach 1.
The first student to show their work gets a participation point.
In-class: Raise your hand.
Online: Use “raise hand” function in WebEx.
Remainder

## Slide 17: Decimal to Binary by Short Division
223 = ?2
223
112 1
56 0
28 0
14 0
7 0
4 1
2 0
1
2
2
2
2
2
2
2
2
Read back upwards
101000012
Remainder

## Slide 18: Quick Detour Binary’s brothers: the oct and the hex
100011012
0b10001101
0215
2158
Binary Numbers (“bin”)
Octal (“oct”)
Hexadecimal (“hex”)
0x8C
8C16
Notes: In the world of engineering and computing, there are also two more important number bases, the octal system (0-7) and the hexadecimal system (0-F).
The octal system is not much used, but it can appear sometimes if you’re working with triplets of binary data. On the other hand, hex is widely used everywhere especially to compact binary numbers.

## Slide 19: Quick Detour Binary’s brothers: the oct and the hex
bin  hex and bin  oct conversion is very easy!
100011012
2158
8C16
8 = 23 so one digit in oct = 3 digits in bin.
16 = 24 so one digit in oct = 4 digits in bin.

## Slide 20: Analog and Digital … where binary is used, a lot.
Computers are actually trillions of electronic switches and signals.
Electronic systems can work on either:
Voltage (V)
Time
Analog System
Voltage (V)
Time
Digital System
Conversion from A=>D involves sampling and quantization.
Notes: It’s much easier to operate on digital signals than analog ones.
While circuits that work with digital signals are more complex and require more engineering, operating and programming with digital circuits is much easier to understand. I can show you my transcript for undergraduate, and let’s hope we agree on this one :(

## Slide 21: Discussion
Are digital computers “accurate”?
How do they work with natural information like noise and light?

## Slide 22: Sampling Example
Accurate quantization and sampling requires more bits.
Software used: Audacity 2.1.2 © Audacity Team; Data: generated using this software.
8 kbps, 8000 Hz sampling
320 kbps, 48000 Hz sampling

## Slide 23: Arithmetic Operations
Addition
Subtraction
Multiplication
Division and Modulo (same operation!)
It doesn’t end like you think …
Note: We’ll discuss addition and multiplication today.

## Slide 24: Addition
36 + 29 = 1001102 + 0111012
1001102
+0111012
2
Learn More:
https://www.sciencedirect.com/topics/computer-science/binary-addition

## Slide 25: Two kinds of operations in adding
112
+012
02
1
Adding
Carrying

## Slide 26: Discussion
Is binary arithmetic easier than decimal? Why?

## Slide 27: Negative Numbers in Digital Logic: 2’s Complement
010100012
There are no minus signs in digital logic, so John von Neumann invented something cool: Two’s Complement.
81 =
101011102
Flip all bits
Then add 1
101011112
For this to work, we need another zero bit up front.
= -81 … ?

## Slide 28: 2’s Complement (cont.) Now try it.
010100012
+101011112
1000000002
Disregard this bit. If we are working with 8-bit computer, it has no place.
Participation Point! Can someone help me add this?

## Slide 29: Why computers do not really have subtraction?
Addition = Add and Carry operations
Subtraction (arithmetic) = Subtract and Borrow operations
Subtraction (computer) = 2’s Complement and Addition {Add & Carry}!

## Slide 30: Multiplication: Decimal
22
×34
88
66
22×4
22×3
748

## Slide 31: Multiplication: Binary
10012
×10112
EASIER than decimal multiplication!
1001
0000
1001
1001
11000112
Shifting Operation
Σ
Add Operation
Filtering Operation

## Slide 32: Logical Operations
Work on each bit at a time.
Good for signal control and manipulation.
Integrated Circuit full of Different Operations and Stuff ※
※ This is traditionally called a black box. Black in this case means “cannot see the inside.”
Input A
Input B
Output X
Output Y
1100 1100 0101 0010
1111 0000 1111 0000
1100 0000 0101 0000
0011 0011 1010 1101
Bonus point!: What are Output X and Y, logically?

## Slide 33: Logical Operators and Logic Gates
A | B | X = A ∧ B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A
B
X
AND Gate
A | B | X = A ∨ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
OR Gate
A
B
X
※ You can also use “X = A AND B” and “X = A OR B” respectively.

## Slide 34: Logical Operators and Logic Gates
A | B | X = A ⊕ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
X
XOR Gate
A | X = ¬A
0 | 1
1 | 0
Inverter (“NOT”)
A
X

## Slide 35: NAND, NOR, and XNOR
They provide opposite results from AND, OR, XOR respectively.
A | B | X = ¬(A ∧ B)
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A | B | X = ¬(A ∨ B)
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | X = ¬(A ⊕ B)
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A
B
X
NAND Gate
NOR Gate
A
B
X
A
B
X
XNOR Gate

## Slide 36: Multiple-Input Gates
Both logical math and logic gates can extend to more than two operands (where it makes sense).
A
B
X
C
A | B | C | X = A ∧ B ∧ C
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 37: 4-way crossovers in Electrical Diagrams
This is how to correctly draw 4-way crossovers in electrical diagrams (and logic gate diagrams).
This class follows either old or recommended style.
Jumping is always better than no-dot crossing, but sometimes it is inconvenient in most drawing tools.
(Three-way junctions should also have dots, but PPT can’t draw them automatically.)
https://en.wikipedia.org/wiki/Circuit_diagram#/media/File:Wire_Crossover_Symbols_for_Circuit_Diagrams.png

## Slide 38: Combining them together, we can achieve a lot of results.
Bonus Point: What is this circuit? Explain in human language!
Input A
Input B
Input C
Output W
Output X
Output Y
Output Z

## Slide 39: Hint: Trace one output at a time.
Input A
Input B
Input C
Output W
Output X
Output Y
Output Z
W = (A ∧ B) ∧ C

## Slide 40: Hint: Trace one output at a time.
Input A
Input B
Input C
Output W
Output X
Output Y
Output Z
Download the slide from LMS and try later from your home 

## Slide 41: Logic Gate Simulation
You can try various tools for logic gate simulation if you want to understand them better.
We’ll be using many kinds of simulators throughout the class, and you can also use them for your reports too. Get used to them 
https://circuitverse.org/simulator
https://academo.org/demos/logic-gate-simulator/

## Slide 42: Logic to Arithmetic: Half Adders
Input A
Input B
Sum
Carry
A | B | C = A ∧ B | S = A ⊕ B
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Circuit contains both adding and carrying!

## Slide 43: Logic to Operations: SR Latch
※ The official KU textbook uses the term “RS Flip-Flop” which is the same.
The difference is that the textbook illustrates a NAND SR Latch. Here we use NOR SR Latch.
They both achieve same results.
S (Set) | R (Reset) |  | 
0 | 0 | Keep State | 
1 | 0 | 1 | 0
0 | 1 | 0 | 1
1 | 1 | Invalid | 
S (Set) | R (Reset) |  | 
0 | 0 | Keep State | 
1 | 0 | 1 | 0
0 | 1 | 0 | 1
1 | 1 | Invalid | 

## Slide 44: Wait! Is that memory?
It took humanity about 300 years from the first definition of electricity by William Gilbert to creating the first flip-flop.
(A modern smartphone with 256 GB memory contains about 2,048,000,000,000 bits.)
0/1
Achievement Unlocked!
A Little Bit!
We just (re)discovered 1 bit of memory!

## Slide 45: In-Class Activity
Create a circuit diagram and a truth table for the following expression:
X = (A ∧ B) ∨ C

## Slide 46: In-Class Activity
X = (A ∧ B) ∨ C

## Slide 47: In-Class Activity
X = (A ∧ B) ∨ C
Input A
Input B

## Slide 48: In-Class Activity
X = (A ∧ B) ∨ C
Input A
Input B
Input C
Output X

## Slide 49: In-Class Activity
X = (A ∧ B) ∨ C
A
B
C
X
A | B | C | A ∧ B | (A ∧ B) ∨ C
0 |  |  |  | 
0 |  |  |  | 
0 |  |  |  | 
0 |  |  |  | 
1 |  |  |  | 
1 |  |  |  | 
1 |  |  |  | 
1 |  |  |  | 
Copy Here
Paste Here

## Slide 50: In-Class Activity
X = (A ∧ B) ∨ C
A
B
C
X
A | B | C | A ∧ B | (A ∧ B) ∨ C
0 | 0 |  |  | 
0 | 0 |  |  | 
0 | 1 |  |  | 
0 | 1 |  |  | 
1 | 0 |  |  | 
1 | 0 |  |  | 
1 | 1 |  |  | 
1 | 1 |  |  | 

## Slide 51: In-Class Activity
X = (A ∧ B) ∨ C
A
B
C
X
A | B | C | A ∧ B | (A ∧ B) ∨ C
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 

## Slide 52: In-Class Activity
X = (A ∧ B) ∨ C
A
B
C
X
A | B | C | A ∧ B | (A ∧ B) ∨ C
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 1
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 1
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 1
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 1
If C is 1, then X is immediately 1.

## Slide 53: In-Class Activity
X = (A ∧ B) ∨ C
A
B
C
X
A | B | C | A ∧ B | (A ∧ B) ∨ C
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 1 | 1
Fill in the logic for A AND B.

## Slide 54: In-Class Activity
X = (A ∧ B) ∨ C
A
B
C
X
A | B | C | A ∧ B | (A ∧ B) ∨ C
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
Compute the rest of the logic.

## Slide 55: In-Class Activity
X = (A ∧ B) ∨ C
A
B
C
X
A | B | C | A ∧ B | (A ∧ B) ∨ C
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
Done.

## Slide 56: Logic gates in ICs
This is the 7400 IC.
You may notice the dot at the end of OR. This is the NOR gate.
There are hundreds of millions of these gates in a CPU.
By Tosaka - Author's original, CC BY 3.0, https://commons.wikimedia.org/w/index.php?curid=6518691

## Slide 57: Binary in the Nature
There is one important that work “similar” to binary. It’s actually our DNA.
https://en.wikipedia.org/wiki/DNA_codon_table

## Slide 58: Wait, what?
There are 4 bases, right? We can try to represent:
DNA Base | Binary
T | 00
C | 01
A | 10
G | 11
Note: This is a simplification.

## Slide 59: Store DNA information in binary!
atgagagcggtccatctccttgcggtgagc
DNA Base | Binary
T | 00
C | 01
A | 10
G | 11
100011 101110 110111 110001 011000 010001 010000 110111 110011 101101
30 bases
60 bits = ~ 8 bytes
※
NOTE AGAIN: This is just a sample hypothetical case!
Human Genome = 3 BILLION bases => 750 Megabytes PER PERSON AT LEAST. (Just the data)
Download human genome at https://www.gencodegenes.org/human/
(FASTA file for ALL regions = 800+ MB compressed)

## Slide 60: And, store binary information in DNA …

## Slide 61: Discussion
How can we represent other things in binary form?
What do you think about using DNA as data storage?