## Slide 1: Information Science
Lecture 5: Data Communication and Computer Networks
Asst. Prof. Chawanat Nakasan | 2021-11-02
GSCI1801A
Enhanced Edition: 2021-11-05

## Slide 2: Enhanced Edition
This slide file has been modified from its original version for better clarity.
Slide numbers may change, but none of the original content was removed.
It is safe for current students to use this file for study and examination reference.
Most of this information is presented from a “for users” perspective. This is because the goal of this class is for you to have appreciation for information science (know what we study and hopefully like it enough to learn more), not to become the next John von Neumann or Ada Lovelace.

## Slide 3: Class Announcement
Report 1 is due next week.
レポート１の締め切りは来週です。
Submission closes 2021-11-09 11:59:59 JST.
Late submissions lose 20% points per day.

## Slide 4: Agenda
Data Communication
Network Concepts
Exploring the TCP/IP Protocol Model

## Slide 5: ⚠️ Please save the slides! ⚠️
Content presented here is more detailed than the 情報の科学 official textbook.
Slides can be downloaded from the LMS.
Content from the slide may be on exam.

## Slide 6: Data Communication

## Slide 7
“the act or process of using words, sounds, signs, or behaviors to express or exchange information or to express your ideas, thoughts, feelings, etc., to someone else” – Merriam-Webster
“to share information with others by speaking, writing, moving your body, or using other signals” – Cambridge Dictionary
“If you communicate with someone, you share or exchange information with them, for example by speaking, writing, or using equipment. You can also say that two people communicate.” – Collins Dictionary
share or exchange information, or express ideas
with someone else
by speaking, writing, moving your body, using equipment, or signals
“the activity or process of expressing ideas and feelings or of giving people information” – Oxford Learner’s Dictionary

## Slide 8: Communication Model (Modified and Interpreted for Data Communication)
S
E
C
D
R
Noise Source
Noise
Message
Signal
Received Signal
Received Message
M
S
S’
M’
This model is based on Shannon Model and Berlo’s SMCR Model.
Sender
Encoder
(modulator)
Decoder
(demodulator)
Recipient
Message =
Content
Structure
Code
Signal = Signaling method, etc.
Channel = Usually physical media + bandwidth, etc.

## Slide 9: Network Concepts

## Slide 10: The Post/Mail/Courier Model Human Communication, Data Communication, sending things, all the same. (Use whichever word you remember.)
🚚
Load
Pack
Send
Receive
Unpack
Get

## Slide 11: The Packet Model: Handling Large Data Sizes
1
🚚
2
🚚
3
🚚
4
🚚
5
🚚
6
🚚
Split data
Pack and encapsulate
Transmission

## Slide 12: The Packet Model: Handling Different Data Formats
A packet containing data.
All packets look and behave the same.
There are many kinds of data.

## Slide 13: Abstraction
Once the item leaves your hands, you can rest assured it will arrive. The delivery is someone else’s problem.
You can assume that the delivery will somehow complete.
Death Stranding / Kojima Productions, via Gosunoob
You can sleep easy!
It’s his problem now.
Cat Photo: Own Work, Cat is a staff member at Mikan Neko Cat Cafe, Kurashiki

## Slide 14: The Network Stack
Therefore, the network is all about processes:
Processing it for transmission
Receiving input
Passing it along
Processing it for reception
Passing it along
Receiving input
(Sending side)
(Receiving side)

## Slide 15: The Network Stack
Since communication creates multiple levels of information processing, this results in a “stack” of many layers.
Layer 5
Layer 4
Layer 3
Layer 2
Layer 1
Layer 5
Layer 4
Layer 3
Layer 2
Layer 1
L1-Protocol
L2-Protocol
L3-Protocol
L4-Protocol
L5-Protocol
Vertical compatibility:
Protocols work with other protocols in nearby layers of the same machine.
Horizontal compatibility:
Protocols work with same protocols across the network

## Slide 16: Open Systems Interconnection (OSI) Model
This concept of a network stack is formalized into a global standard.
The ISO (International Organization for Standardization) defines the OSI Model (Open Systems Interconnection Model) as a 7-layer system of computer network elements.
OSI-L1
OSI-L2
OSI-L3
OSI-L4
OSI-L5
OSI-L6
OSI-L7
Physical Layer
Data Link Layer
Network Layer
Transport Layer
Session Layer
Presentation Layer
Application Layer

## Slide 17: Open Systems Interconnection (OSI) Model
OSI-L1
OSI-L2
OSI-L3
OSI-L4
OSI-L5
OSI-L6
OSI-L7
Physical Layer
Data Link Layer
Network Layer
Transport Layer
Session Layer
Presentation Layer
Application Layer
Defines how data is physically sent across the network, such as by wire and radio signals.
Provides communication within same network.
Provides abstraction of physical layer properties.
Provides addressing and routing between networks (across the Internet) on an individual packet basis.
Provides abstraction of applications into port numbers (multiplexing) and provides consistency (packet in-order) and speed (congestion) control.
Provides session creation and maintenance (“logging in”) and manages long-term connections e.g. SOCKS and PAP.
Data encoding and translation, such as data type definition (MIME types), character systems (ASCII), etc.
Provides functional utility to the user or system operations, such as web content (HTTP), email (SMTP), and network configuration (DHCP).
Don’t worry for now. Just keep this for your reference.

## Slide 18: The TCP/IP Protocol Model
The TCP/IP Protocol Suite reduces some layers from the OSI model and changes some definitions.
It is considered more practical for general, research, and educational use.
There are many forms of TCP/IP Protocol Models, but in this class, we will use this model.
  Kanazawa University official textbook uses a 4-layer model.
Physical Layer
Data Link Layer
Network Layer
Transport Layer
Application Layer

## Slide 19: Comparison between OSI and TCP/IP Protocol Model
Physical Layer
Data Link Layer
Network Layer
Transport Layer
Application Layer
OSI-L1
OSI-L2
OSI-L3
OSI-L4
OSI-L5
OSI-L6
OSI-L7
Physical Layer
Data Link Layer
Network Layer
Transport Layer
Session Layer
Presentation Layer
Application Layer
OSI Model
TCP/IP Protocol Model

## Slide 20: Addressing
Addressing allows the network elements to send to the correct destination.
It’s very similar to writing an address.
Different protocols use different kinds of addresses.
Part of the envelope analogy also lets us explore the concepts of encapsulation!
920-1192
石川県金沢市角間町
金沢大学 学術メディア創成センター
角間 あざみ 様
EMI 角間あざみ 様
Locally (in-campus) addressed envelope
Postal addressing

## Slide 21: Encapsulation
Application
Transport
Network
Message
Message
Message
Message
App-Header
App-Header
App-Header
Transp.-Header
Transp.-Header
Data Link
Physical
Net-Header
Message
App-Header
Transp.-Header
Net-Header
Link-Header

## Slide 22: Signal Modulation
Modulation
Demodulation
“MODEM”
= [01]*
(Data sequence)
(Signal)
Message
App-Header
Transp.-Header
Net-Header
Link-Header

## Slide 23: Hey, we’re at the bottom of the stack!
Physical Layer
Data Link Layer
Network Layer
Transport Layer
Application Layer
TCP/IP Protocol Model
Wired (有線)
Wireless (無線)

## Slide 24: Types of Wired Media
Wired
Wireless
Copper Cables
Optical Cables (“Hikari”)
Twisted-Pair Cables (“LAN Cables”)
Coaxial Cables
(“Subscriber TV / CATV Cables”)
Image Sources:
Twisted-Pair Cable: Raysonho @ Open Grid Scheduler / Grid Engine
Coaxial Cable: Arj / Wikipedia

## Slide 25: Twisted Pair Cables
Image Source: Baran Ivo / Wikipedia

## Slide 26: How to choose cables?
Formally called Ethernet Cables, there are two popular ways to indicate a cable.
“Cat” System
(Common “market” language)
Cat 5e = Supports Gigabit Ethernet
Cat 6 = Supports 10Gig Ethernet
etc.
“Specification” System
Pros:
Easy to understand by consumers
Higher number is always more modern
Cons:
Does not reflect actual specification of the cable
Max Data Rate
10
100
1000
10G
“Baseband”
BASE
“Cable Class”
2 = up to 200 m
5 = up to 500 m
T = Twisted Pair
X = only 2 pairs used
F = Fiber Optic
Pros:
Very specific and you’re likely to get what you want if you order by this specification system.
Cons:
Most consumers don’t understand this system.
Example: 1000BASE-T = 1 Gigabit Twisted-Pair Cable

## Slide 27: What about non-BASE things?
If it isn’t BASE(band), then it’s BROAD(band).
Broadband means multiple ranges of transmission frequency is mixed into the cable. Examples include “broadband internet” that uses multiple data channels.
If you have heard of the term “DOCSIS”, this is the formal term for what most of us use for broadband internet.
Broadband cables for ethernet is rare. There is a cable called 10BROAD36 (10 Mbps broadband over 3600 meters), but nobody really uses it.
You don’t have to worry about broadband cables. It will not be in the exam. (You will seriously learn about this if you go to a telecom company. They will pay you to learn about it.)
※ This is an enhanced edition slide not included during live presentation.
Baseband communication has only one base frequency.
There is no sense of “channels” here.
Broadband communication has many “channels”.
The “modem” at each side will merge/split these channels.
Typical cases of broadband communications include:
Digital Subscriber Line (DSL): Phone Voice + Internet
Cable Television (CATV): Television + Internet

## Slide 28: Going Over 100m?
Most ethernet cables nowadays no longer support over 100m lengths. Here are some suggested solutions:
Using repeaters or chain with switches.
Using fiber optic systems. High upfront cost, but very high performance and can cover great distances.
Using wireless solutions is great when laying wires is expensive or impossible (two office buildings on two sides of public road, etc.)
※ This is an enhanced edition slide not included during live presentation.

## Slide 29: Example of properly labeled commercial (home-use) cables
Source: Commercial product being reviewed and critiqued.
“Cat” number
40GBASE-T =
up to 40 Gbps
baseband
twisted pair
Clear technical specs and compatibility list
Straight or crossover cable. Some old devices require crossover, like switch-to-switch or PC-to-PC connections.
This is not a major concern nowadays.
Cable length
Cable thickness and power-over-ethernet support (good for CCTVs and IoT)
※ This is an enhanced edition slide not included during live presentation.

## Slide 30: Example of dubiously labeled product (not as good, but enough information)
“Cat” number
Cable length
We can infer that this “Cat5e” (based on our knowledge) is a 1000Base-T cable. At least we know what we’re buying here.
Source: Commercial product being reviewed and critiqued.
※ This is an enhanced edition slide not included during live presentation.

## Slide 31: Example of poorly labeled product
No product name
(“LAN” is not adequate as a product name)
Only length is indicated
No category or other specification
There might be something on the back, but it’s probably just company address and barcode.
Anyway, we can’t see it here, so I’m not going to buy this brand online.
Do you trust this manufacturer?
Source: Commercial product being reviewed and critiqued.
※ This is an enhanced edition slide not included during live presentation.

## Slide 32: Wireless Communication
Wired
Wireless
Local Network
Mobile Network
Satellite
Wi-Fi
Bluetooth
3G
4G
5G
Terrestrial
Microwave
Other Radio Techniques (SSB, etc.)

## Slide 33: Wi-Fi
IEEE 802.11
More Recent
Standard | Max Data Rate | Frequency Band | Going through walls
a | 54 Mbps | 5 GHz | △
b | 11 Mbps | 2.4 GHz | 〇
g | 54 Mbps | 2.4 GHz | 〇
n | 600 Mbps | 2.4 GHz | 〇
 |  | 5 GHz | △
ac | 6.9 Gbps | 2.4 GHz | 〇
ax | 9.6 Gbps | 2.4 GHz | 〇
 |  | 5 GHz | △
This is “Wi-Fi 6”

## Slide 34: 5G Emerging Tech: mmWave vs Sub6 … what’s going on?
Graphics: Inductiveload, NASA / Wikipedia; Britannica
Most home telecommunications today occur in this range.

## Slide 35: Comparison of 2G~5G by frequency range
Graphics : Britannica. Frequency ranges are approximate.
5G mmWave
5G Sub6
2G: GSM/GPRS/EDGE
3G: UMTS/FOMA
4G: WIMAX/LTE
Wi-Fi = 2.4 or 5 GHz

## Slide 36: mmWave vs Sub6
mmWave
Higher frequency (30-300 GHz)
Harder to go through buildings (“line-of-sight”)
Less coverage
Requires specific phone models (as of 2021)
  mmWave compatible hardware is expensive at the moment.
Sub6
Lower frequency (Sub6 = “less than 6 GHz”)
Easier to go through buildings
Better coverage
More compatible models
Personal comments: Unless you live in a big city and confirmed that your carrier supports mmWave, you probably don’t need to pay for devices that support it for now.

## Slide 37: Data Link Layer
Physical Layer
Data Link Layer
Network Layer
Transport Layer
Application Layer
TCP/IP Protocol Model

## Slide 38: Roles of the Data Link Layer
Lowest abstraction level possible
Collision detection
Error detection
Stop sending when others are sending
Packet Switching

## Slide 39: More things in Data Link Layer
MAC Address
D8-12-E9-7B-2C-C1
D8-12-E9-7B-2C-C3
D8-12-E9-7B-2C-C4
D8-12-E9-7B-2C-C0
D8-12-E9-7B-2C-C2

## Slide 40: Your device may have more than one MAC address.
2D-3B-8D-20-A4-AC
00-18-C2-6C-40-8D
One MAC address is (supposed to be) globally unique.

## Slide 41: Network Layer: The Internet Protocol
Physical Layer
Data Link Layer
Network Layer
Transport Layer
Application Layer
TCP/IP Protocol Model
163.221.222.222
158.108.8.7

## Slide 42: Key roles of the Internet Protocol
Internetwork Routing
IP Address as Globally Unique Address System
Provides a common format for packets
Pretty much all protocols in the world rely on IP.
There are no repeated IP addresses on the global scale.
Internetwork = Between the networks.
IP is the basis of the Internet itself.

## Slide 43: How to check your MAC and IP addresses (Windows)
Start command prompt
Type “ipconfig /all”
Do not share this information without technical need.
Ethernet adapter Ethernet 2:
Connection-specific DNS Suffix . :
Description . . . . . . . . . . . : Intel(R) Ethernet Connection (7) I219-V
Physical Address. . . . . . . . . : A8-A1-59-03-XX-XX
DHCP Enabled. . . . . . . . . . . : Yes
Autoconfiguration Enabled . . . . : Yes
Link-local IPv6 Address . . . . . : fe80::5886:7093:b8a2:7608%14(Preferred)
IPv4 Address. . . . . . . . . . . : 172.16.20.2(Preferred)
Subnet Mask . . . . . . . . . . . : 255.255.0.0
Lease Obtained. . . . . . . . . . : Sunday, October 24, 2021 18:36:39
Lease Expires . . . . . . . . . . : Tuesday, November 2, 2021 11:17:16
Default Gateway . . . . . . . . . : 172.16.0.1
DHCP Server . . . . . . . . . . . : 172.16.0.1
DHCPv6 IAID . . . . . . . . . . . : 195600729
DHCPv6 Client DUID. . . . . . . . : 00-01-00-01-28-03-18-C5-A8-A1-59-03-XX-XX
DNS Servers . . . . . . . . . . . : 172.16.0.1
8.8.8.8
8.8.4.4
NetBIOS over Tcpip. . . . . . . . : Enabled

## Slide 44: Difference between MAC and IP addresses
MAC Address
Address for data link layer
Used for routing within network
Hardware-specific, cannot be changed (conventionally).
IP Address
Address for network layer
Used for routing across networks
Can be configured by the OS.
Usually, one interface has one MAC address and one IP address.
In more advanced network configurations, this may change.

## Slide 45: Transport Layer
Physical Layer
Data Link Layer
Network Layer
Transport Layer
Application Layer
TCP/IP Protocol Model
TCP
Transmission Control Protocol
(Connection-oriented)
UDP
User Datagram Protocol
(Connectionless)

## Slide 46: This is where port numbers are!
Each computer can run multiple processes at a time.
Port numbers allow you to guide network traffic to each process.
IP Address: 10.0.0.8
:22 = ssh (remote control)
:80 = web server
:8080 = another web server
Full list of all common port numbers: https://www.iana.org/assignments/service-names-port-numbers/service-names-port-numbers.xhtml
:68 = bootp/dhcp (network configuration)
If you want to connect to this computer using ssh,
you should access “10.0.0.8:22”.

## Slide 47: What TCP does that UDP doesn’t?
Connections
  TCP has a sense of connections being open or closed, which allows TCP to implement the following features!
Congestion control
  Adjust communication speed when the network is busy.
Packet ordering
  TCP keeps track of packet order, so they arrive “in-order”.
Error Detection and Retransmission
  TCP can detect errors and resend packets if they fail. The data recipient reports the errors back to the sender.

## Slide 48: General uses of UDP and TCP
When to use UDP
When small amounts of packet errors is OK.
When your application is small and does very simple quick things.
When you have more networking than device memory (using embedded/small hardware)
Applications include:
  media streaming
  telemetry (device data) streaming
  real-time gaming (FPS, etc.)
When to use TCP
When you need total correctness of the data.
When you need the security features of TCP.

## Slide 49: Finally, we’re at the application layer!
Lots of functionality is provided here, and this layer has the greatest variety of protocols and applications.
Physical Layer
Data Link Layer
Network Layer
Transport Layer
Application Layer
TCP/IP Protocol Model

## Slide 50: Examples of Application-Layer Protocols
Domain Name Services (DNS)
>nslookup kanazawa-u.ac.jp
Server: UnKnown
Address: 172.16.0.1
Non-authoritative answer:
Name: kanazawa-u.ac.jp
Address: 133.28.0.180
Hypertext Transfer Protocol (HTTP)
The main protocol for the World Wide Web
Message Queue Telemetry Transport (MQTT)
Very prominent in Internet of Things
Extensible Messaging and Presence Protocol (XMPP)
Some chat apps use this protocol.
Trademarks are owned by their respective owners.

## Slide 51: Examples of Application-Layer Protocols
Can anyone give me an IP address?
Okay, I got 10.0.0.9 for you. Your default gateway and DNS are 10.0.0.1. Is this OK?
Great. Please do.
OK. All done!
Dynamic Host Configuration Protocol (DHCP)

## Slide 52: And so on!
There are hundreds of application layer protocols. More are being developed every day.
You don’t have to remember the details. The most important thing today is to understand the context of things so it’s easier for you to learn in the future.

## Slide 53: What can you learn further in single sentences?
Virtual Private Network (VPN)
  Encapsulate and encrypt total data transmission to achieve privacy.
Internet of Things (IoT)
  Many small devices communicate and provide useful functionality in physical world.
Personal Area Network (PAN)
  Things around your body that communicate with each other.
Blockchain
  Using concepts in computer networks, computation, and security to create a tamper-proof public record system.
  We’ll talk about this later!

## Slide 54: Class Announcement (again)
Report 1 is due next week.
レポート１の締め切りは来週です。
Submission closes 2021-11-09 11:59:59 JST.
Late submissions lose 20% points per day.

## Slide 55: That’s all for today!
Graphics (characters): Lunatic Company, used with explicit permission.

## Slide 56: Fair Use Indicator (If you want to copy my slides for personal use)
See slide number below.
If the number is gray, you are okay. All content (text, pictures, etc.) is mine.
If the number is blue, some content belongs to Kanazawa University. It might be okay for personal use.
If the number is red, some content belongs to non-KU entity. Copy with caution.
  This includes Microsoft icons and clip-arts, but not shapes, fonts, and styles that come with PowerPoint itself.
If a slide contains both blue and red content, the number will be red.