## Slide 1: Computer Science and Information Processing
Lecture 1: Computer and Architecture, and Basic Operations in Computer Science
Asst. Prof. Chawanat Nakasan | 2019-06-11
GSCI1801A

## Slide 2: Agenda
What’s a computer?
What’s inside a computer?
  Explanation of various components
Computer Architecture
Binary Number System
Arithmetic Operations
Logical Operations

## Slide 3: What’s a computer?
a machine that can be programmed to manipulate symbols. Its principal characteristics are:
  It responds to a specific set of instructions in a well-defined manner.
  It can execute a prerecorded list of instructions (a program).
  It can quickly store and retrieve large amounts of data.
https://www.cs.cmu.edu/~fgandon/lecture/uk1999/computers_types/

## Slide 4: How fast is a computer?
ENIAC, 1945 (USA)
Speed: 5,000 cycles per second
ABCI, 2018 (Japan)
Speed: 37 PFLOPS (high precision real numbers)
In less than a century, world-leading computers got faster by at least 7 billion-fold.

## Slide 5: How fast is a computer? (Web Distribution Version)
ENIAC, 1945 (USA)
  Speed: 5,000 cycles per second
ABCI, 2018 (Japan)
  Speed: 37 PFLOPS (high precision real numbers)
In less than a century, world-leading computers got faster by at least 7 billion-fold.

## Slide 6: What’s in a (typical) computer?
Expansion (PCI)
GPU(s)
SSDs (card type)
Extra I/O
Extra Network
Primary Memory
(RAM)
Heatsink & Fan
Power Supply
I/O
USB Ports
Network Interface
Sound Jack
etc.
Secondary Memory: SATA Ports
HDDs & SSDs (cable type)
Other devices (BD, DVD, …)
CPU
Notes: Secret Question:
Can you have multiple GPUs? How do they work?
Can you have multiple network interfaces? How do they work?

## Slide 7: Basic Computer Architecture [[von Neumann Architecture]]
Processor (“CPU”)
Input Devices
Output Devices
Storage
(May be on or off motherboard)
Control Unit (CU)
Arithmetic Logic Unit (ALU)
Registers and Cache (considered as storage on CPU)
Examples of Storage: RAM Hard Drives Removable Storage
Examples of Output: Display Sound Printer Network Interface*
Examples of Input: Keyboard Mouse Network Interface*
*Network Interface is a funny oddball and will be greatly explained later!

## Slide 8: Memory Hierarchy
In CPU
On Board
Register
Cache
RAM
Solid-State Drives (SSD) (slotted type)
In Enclosure
Hard-Disk Drive
Solid-State Drives (SSD) (cable type)
External / Removable
faster, smaller, more expensive
slower, larger more affordable
Removable Media Back-Up Drives Networked Storage

## Slide 9: Binary number system

## Slide 10: Binary Number System
Conversion from/to Decimal
Representing negative numbers
Why it’s easier than decimal?
Binary systems in the nature

## Slide 11: What is decimal number?
4,482,692,653
4,000,000,000
400,000,000
80,000,000
2,000,000
600,000
90,000
2,000
600
50
3
4×109
4×108
8×107
2×106
6×105
9×104
2×103
6×102
5×101
3×100

## Slide 12: Now, what is binary number?
11101010
10000000
1000000
100000
00000
1000
000
10
0
1×27 = 128
1×26 = 64
1×25 = 32
0×24 = 0
1×23 = 8
0×22 = 0
1×21 = 2
0×20 = 0
>> This part is decimal
234

## Slide 13: Indicating Numbers by Bases
100011012
10001101
1000110110
0b10001101
Programming Style
Using Subscripts
Binary Numbers (“bin”)
Decimal Numbers (“dec”)

## Slide 14: A Bit and a Byte
100011012
This is a bit.
8 bits make a byte.
Bit is the smallest digital information possible.
A lot more meaningful data in computers are in bytes, such as characters (1 or 2 bytes) and numbers (1-8 bytes).
Files are almost never stored by individual bits.
Notes: Note that a byte used to consist of more or less than 8 bits. Nowadays, it is commonly accepted that 8 bits make a byte, and a character (ASCII. We might get to learn about Unicode later.) is encoded on a per-byte basis.

## Slide 15: Conversion Methods
Binary to Decimal
Decimal to Binary
Position value method (earlier)
Short division method
Position value method
Notes: The position value method is just math we showed earlier. The fun method is the short division.

## Slide 16: Decimal to Binary by Short Division
223 = ?2
223
112 1
2

## Slide 17: Decimal to Binary by Short Division
223 = ?2
223
112 1
56 0
2
2
Participation Point! Please continue dividing until you reach 1.

## Slide 18: Decimal to Binary by Short Division
223 = ?2
223
112 1
56 0
28 0
14 0
7 0
4 1
2 0
1
2
2
2
2
2
2
2
2
Read back upwards
101000012

## Slide 19: Quick Detour Binary’s brothers: the oct and the hex
100011012
0b10001101
0215
2158
Binary Numbers (“bin”)
Octal (“oct”)
Hexadecimal (“hex”)
0x8C
8C16
Notes: In the world of engineering and computing, there are also two more important number bases, the octal system (0-7) and the hexadecimal system (0-F).
The octal system is not much used, but it can appear sometimes if you’re working with triplets of binary data. On the other hand, hex is widely used everywhere especially to compact binary numbers.

## Slide 20: Quick Detour Binary’s brothers: the oct and the hex
bin  hex and bin  oct conversion is very easy!
100011012
2158
8C16
8 = 23 so one digit in oct = 3 digits in bin.
16 = 24 so one digit in oct = 4 digits in bin.

## Slide 21: Analog and Digital … where binary is used, a lot.
Computers are actually trillions of electronic switches and signals.
Electronic systems can work on either:
Voltage (V)
Time
Analog System
Voltage (V)
Time
Digital System
Conversion from A=>D involves sampling and quantization.
Notes: It’s much easier to operate on digital signals than analog ones.
While circuits that work with digital signals are more complex and require more engineering, operating and programming with digital circuits is much easier to understand. I can show you my transcript for undergraduate, and let’s hope we agree on this one :(

## Slide 22: Discussion
Are digital computers “accurate”?
How do they work with natural information like noise and light?

## Slide 23: Sampling Example
Accurate sampling & quantization requires more bits.
Software used: Audacity 2.1.2 © Audacity Team; Data: generated using this software.
8 kbps, 8000 Hz sampling
320 kbps, 48000 Hz sampling

## Slide 24: Arithmetic Operations
Addition
Subtraction
Multiplication
Division and Modulo (same operation!)
It doesn’t end like you think …
Note: We’ll discuss addition and multiplication today.

## Slide 25: Addition
36 + 29 = 1001102 + 0111012
1001102
+0111012
2
Learn More:
https://www.sciencedirect.com/topics/computer-science/binary-addition

## Slide 26: Two kinds of operations in adding
112
+012
02
1
Adding
Carrying

## Slide 27: Discussion
Is binary arithmetic easier than decimal? Why?

## Slide 28: Negative Numbers in Digital Logic: 2’s Complement
010100012
There are no minus signs in digital logic, so John von Neumann invented something cool: Two’s Complement.
81 =
101011102
Flip all bits
Then add 1
101011112
For this to work, we need another zero bit up front.
= -81 … ?

## Slide 29: 2’s Complement (cont.) Now try it.
010100012
+101011112
1000000002
Disregard this bit. If we are working with 8-bit computer, it has no place.
Participation Point! Can someone help me add this?

## Slide 30: Why computers do not really have subtraction?
Addition = Add and Carry operations
Subtraction (arithmetic) = Subtract and Borrow operations
Subtraction (computer) = 2’s Complement and Addition {Add & Carry}!

## Slide 31: Multiplication: Decimal
22
×34
88
66
22×4
22×3
748

## Slide 32: Multiplication: Binary
10012
×10112
EASIER than decimal multiplication!
1001
0000
1001
1001
11000112
Shifting Operation
Σ
Add Operation
Filtering Operation

## Slide 33: Logical Operations
Work on each bit at a time.
Good for signal control and manipulation.
Integrated Circuit full of Different Operations and Stuff ※
※ This is traditionally called a black box. Black in this case means “cannot see the inside.”
Input A
Input B
Output X
Output Y
1100 1100 0101 0010
1111 0000 1111 0000
1100 0000 0101 0000
0011 0011 1010 1101
Bonus point!: What are Output X and Y, logically?

## Slide 34: Logical Operators and Logic Gates
A | B | X = A ∧ B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A
B
X
AND Gate
A | B | X = A ∨ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
OR Gate
A
B
X

## Slide 35: Logical Operators and Logic Gates
A | B | X = A ⊕ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
X
XOR Gate
A | X = ¬A
0 | 1
1 | 0
Inverter (“NOT”)
A
X

## Slide 36: Multiple-Input Gates
Both logical math and logic gates can extend to more than two operands (where it makes sense).
A
B
X
C
A | B | C | X = A ∧ B ∧ C
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 37: Combining them together, we can achieve a lot of results.
Bonus Point: What is this circuit? Explain in human language!
Input A
Input B
Input C
Output W
Output X
Output Y
Output Z

## Slide 38: Hint: Trace one output at a time.
Input A
Input B
Input C
Output W
Output X
Output Y
Output Z

## Slide 39: Hint: Trace one output at a time.
Input A
Input B
Input C
Output W
Output X
Output Y
Output Z
Download the slide from LMS and try later from your home 

## Slide 40: Logic to Arithmetic: Half Adders
Input A
Input B
Sum
Carry
A | B | C = A ∧ B | S = A ⊕ B
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Circuit contains both adding and carrying!

## Slide 41: Logic gates in ICs
This is the 7400 IC.
You may notice the dot at the end of OR. This is the NOR gate.
There are hundreds of millions of these gates in a CPU.
By Tosaka - Author's original, CC BY 3.0, https://commons.wikimedia.org/w/index.php?curid=6518691

## Slide 42: Binary in the Nature
There is one important that work “similar” to binary. It’s actually our DNA.
https://en.wikipedia.org/wiki/DNA_codon_table

## Slide 43: Wait, what?
There are 4 bases, right? We can try to represent:
DNA Base | Binary
T | 00
C | 01
A | 10
G | 11
Note: It doesn’t work like this.

## Slide 44: Store DNA information in binary!
atgagagcggtccatctccttgcggtgagc
※ (Tani et al., 2015)
First 30 bases of gene data of XoxF methanol dehydrogenase from Methylobacterium aquaticum 22A: https://www.ncbi.nlm.nih.gov/nuccore/NZ_AP014704.1?report=genbank&from=962518&to=964320
DNA Base | Binary
T | 00
C | 01
A | 10
G | 11
100011 101110 110111 110001 011000 010001 010000 110111 110011 101101
30 bases
60 bits = ~ 8 bytes
※
NOTE AGAIN: This is just a sample hypothetical case!
Human Genome = 3 BILLION bases => 750 Megabytes PER PERSON.
(if using this inaccurate method)

## Slide 45: And, store binary information in DNA …

## Slide 46: Discussion
How can we represent other things in binary form?
What do you think about using DNA as data storage?